## Slide 1: HW #6 Workshop
Simple Linked Lists

## Slide 2: General
This is a very simple assignment
You will need a for loop to progressively build the linked list
You will also define a separate function that will print out the contents of the list
  It will receive a pointer to the head of the linked list
  It will then traverse the list, printing out the contents of every node it visits.

## Slide 3: Creating the List
Composed of the following:
  Define the structure to serve as the nodes in the list. It should include:
    An integer member
    A next pointer member
  Define the appropriate data type using typedef
    Include also the pointer type definition to the Node data type. Call it Nodeptr.
  Create the list by defining the head node.
    Set it to NULL

## Slide 4: Before the Loop
  Define a pointer of type Nodeptr. This will be the working pointer that we will use to move about in the list. Let’s call it ptr
  Create the first node outside of the loop. The reason for this is that you must set head to point to it, and this cannot be done repeatedly
    Use malloc() to carve out the block of memory.
    Set head to point to it.
    Set head->next to NULL
    Set ptr to head.
    Set the value of its integer member to 0

## Slide 5: The Loop
  Now create a for loop and set the count to 21.
  In each iteration
    Carve out a memory block using malloc()
    Set ptr->next to the pointer returned by malloc()
    Set ptr to ptr->next
    Set ptr->next to NULL.
    Set the value of the integer member of ptr to the count
    Continue until the count reaches 21
  Finished creating the linked list
  Now let’s print out its contents to make sure

## Slide 6
0
Head
NULL
Head
NULL
0
Head
NULL
Loop
ptr
ptr
ptr->next
0
Head
1
NULL
ptr
ptr->next
0
Head
1
NULL
ptr
ptr->next
Graphically Speaking

## Slide 7: Printout Function
Call the printout function from main() and pass it the head pointer of the linked list
  Double pointer not needed b/c we do not want to make any changes to the head pointer
Define a pointer of type Nodeptr that we will use to move about the list while traversing it
  Call it current
  Set it initially to the pointer passed down from main(), which is the head pointer of the list.

## Slide 8: Printout Function
Write a while loop that continues until the end of the list is reached
  current->next == NULL
At each iteration through the list,
  Use printf() to print out the contents of the integer member of the list